## Slide 1
Machine-Learned Surrogates for Reactive Transport: Numerical and HPC Integration Challenges for Industrial CFD
Thibault Faney

## Slide 2
Refining
Biofuels
Batteries
Chemical processes
Reactive Transport Simulation at IFPEN
Combustion
internal combustion engines
H2 combustion
gas turbines
Flow in porous media
reservoir / basin modeling
EOR
CO2 sequestration
H2 storage

## Slide 3: Issue with traditional solvers
Reactive Transport PDE
Monod system

## Slide 4: Issue with traditional solvers
Reactive Transport PDE
Chemistry operator
  equilibrium or kinetic reactions
  local
  highly non-linear
Solvers
  spatial + time discretization
  splitting vs fully implicit methods
Large amount of local chemistry to be solved at every mesch cell for every time step
  > 75% of total simulation time

## Slide 5: Promise of chemistry surrogate modeling
Constraints in reactive transport
  Geometry
  Initial and Boundary conditions
  Parameters (diffusion coefficients, reaction constants, etc.)
  Chemical system
Redundancy
  inter-simulations (optimisation, control, UQ, real-time)
  intra-simulation (combustion front, mineral dissolution, etc.)
Strong potential of surrogate modeling
  redudancy + space parallelism !

## Slide 6
A Practical example : Thermodynamical Equilibrium

## Slide 7
FLASH calculations
feed composition
P
T
Phase Condition
+
Composition

## Slide 8
SAMPLING
H2O-CH4 binary mixture

## Slide 9
« Black-box » supervised learning model
Integration in Reactive Transport Solver (Vectorization is essential)
Classification Accuracy
Regression MSE = 8,1×10⁻⁵
Results

## Slide 10
« Black-box » supervised learning model
Local, small errors blow up in finite time
Why ? No guarantee on the solution, no physics  no stability
CATACLISM : Coupling AI, Transport And Chemistry for Large-scale Innovative Simulation and Modeling

## Slide 11
« Black-box » supervised learning model
Performance heavily depends on parallelism
GPU not necessarily a clear winner

## Slide 12: Basic Challenges
Numerical challenges
  Precision
  Stability
  Generalisation
Computational challenges
  Fast surrogates

## Slide 13
Some leads and some more challenges

## Slide 14: SAMPLING
High dimensional sampling on simplex (∑𝑧𝑖=1): Dirichlet distribution

## Slide 15: SAMPLING
Unbalanced classes: Add random noise to samples

## Slide 16: SAMPLING
Active Learning

## Slide 17: SAMPLING
Online learning
  Flag bad predictions and add them to database
  Retrain model periodically
New challenges
  UQ for chemistry models
  Move data to GPU to retrain model during computation

## Slide 18: Intrusive Models
Numerical PT-flash calculations for vapor-liquid equilibrium
Update
via the residual approach
The residual approach
P
T
Single phase ?
Yes
No
Phase stability analysis
Phase condition determination
Output
Converge on ?
No
Yes
Initialize distribution coefficients via Wilson approximation
Initialization
Wilson approximation
Successive substitution
Solve Rachford-Rice equation
Rachford-Rice equation
Jingang Qu’s PhD thesis (IFPEN – LIP6 at Sorbonne University)

## Slide 19: Intrusive Models
Data-driven PT-flash calculations for vapor-liquid equilibrium
P
T
Single phase ?
Yes
No
Phase condition determination
Output
Converge on ?
No
Yes
Initialization
Successive substitution
Solve Rachford-Rice equation
NN
proxy classifier
NN proxy initializer
NN proxy calculator

## Slide 20: Intrusive Models
Neural bias of neural networks towards predicting low frequency components of the solution
Good synergy with the quadratic convergence of Newton methods near the solution
1 Jinchao Xu, CEMRACS 2023 Lecture Notes
Poisson equation fit with ReLU activation function1

## Slide 21: Intrusive Models
Convergence guaranteed
Downsides
  Very problem dependent
  “Limited” computational gains
  Requires low latency hybrid HPC / AI computations

## Slide 22: Adding physical constraints
Soft constraints
  Training issues
  Can be difficult to express

## Slide 23: Adding physical constraints
Hard constraints
  Problem dependent
  Gradient issues  hard to train
Y1
Y2
YN
. . .
. . .
Y(t)
Softmax
. . .
Y(t+dt)
. . .

## Slide 24: Adding physical constraints
Hard constraints
  Problem dependent
  Gradient issues  hard to train
Y1
Y2
YN
. . .
. . .
Y(t)
Projection on linear subspace
. . .
Y(t+dt)
. . .

## Slide 25: Adding physical constraints
Results
Conservation of hydrogen mass without (left) and with (right) network enforced mass conservation
Cédric Mehl, IFPEN

## Slide 26: Adding physical constraints
Results
Cédric Mehl, IFPEN

## Slide 27
Challenges

## Slide 28: Challenges with hybrid ML / HPC solvers for reactive transport
Numerical challenges
  Precision and Stability
    Intrusive models
    Physics informed models
    Sampling
    UQ
    Mixed precision integration
    Learn over PDE trajectories
  Generalisation
    One model to rule several chemical systems
    Fondational models
Computational challenges
  Online Learning
  Low latency inference
  Revisiting the performance / accuracy trade-off

## Slide 29: Recommendations
Stability
  A posteriori (trajectory) learning
  Problem dependent structural form for the corrector model
  Adding noise (both a priori and a posteriori)
  Consistency with chemical equations (soft /hard)
  Linearize surrogate model to study stability (eigenvalues)
Generalization
  Use probablistic classifier output (instead of hard classifier)
  Samples need to be representative of the time evolution
  PDE NO : use smooth rhs
  NO with autoencoder trained on base chemical system + retrain to add new species on the fly
Online Learning
  Focus on dynamic local time stepping
  Bayesian model to decide on the fly the use of surrogate model
  Training a very simple domain for inactive chemical points and « track » that domain